OPEN FEED LINES  Z=200 Ohm

Folded dipole

VELOCITY ABOUT : 0.987

TEFLON – SPACER  for lines only 5mm thichness and each 0.5 wl spaced

Can be mounted on metallic structures with PTFE-supports about 20cm long

Balun 100:50 – quarter wave sleeve Balun ( tube range 60mm on 1/4wl coax 75 Ohm; VSWR about 1.1-1.2 in EME band)

# Text boxes

100